## Slide 1: CLCD Functions for SDCC
Chin-Shiuh Shieh

## Slide 2: CLCD Functions for SDCC
clcd.c is a library of Character Liquid Crystal Display (CLCD) functions for Small Device C Compiler (SDCC).

## Slide 3: CLCD Functions for SDCC (cont)

## Slide 4: clcd.c
// Character LCD (HD44780U-compatible) functions
// by CHin-Shiuh Shieh on 2011-04-04
// #define CLCD_RS P2_0
// #define CLCD_RW P2_1
// #define CLCD_E P2_2
// #define CLCD_DB P1
__sbit __at 0xE7 ACC_7;
__code char ASCII[]="0123456789ABCDEF";

## Slide 5: clcd.c (cont)
// Function Prototypes
void clcd_initialize(void);
void clcd_write_instruction(unsigned char instruction);
void clcd_wait(void);
void clcd_cls(void);
void clcd_set_cursor(unsigned int row,unsigned int column);
void clcd_put_char(char c);
void clcd_put_string(char *s);
void clcd_put_byte(unsigned char byte_data);
void clcd_put_word(unsigned int word_data);
void clcd_put_integer(int i);
void i2s(int i,char *s);

## Slide 6: clcd.c (cont)
void clcd_initialize(void)
{
clcd_write_instruction(0x38);
// 8-bit interface, 2 lines, 5x7 dots
clcd_write_instruction(0x0F);
// display on, cursor on, cursor blinking
clcd_write_instruction(0x06);
// move cursor right when read/write
clcd_write_instruction(0x01);
// clear display, cursor home
}

## Slide 7: clcd.c (cont)
void clcd_write_instruction(unsigned char instruction)
{
clcd_wait();
CLCD_RS=0;CLCD_RW=0;
CLCD_DB=instruction;CLCD_E=1;CLCD_E=0;
}
void clcd_wait(void)
{
CLCD_DB=0xFF;
CLCD_RS=0;CLCD_RW=1;
do
{
CLCD_E=1;ACC=CLCD_DB;CLCD_E=0;
}
while(ACC_7==1);
}

## Slide 8: clcd.c (cont)
void clcd_cls(void)
{
clcd_write_instruction(0x01);
}
void clcd_set_cursor(unsigned int row,unsigned int column)
{
unsigned int instruction=0x80;
if(row==1)instruction+=0x40;
instruction+=column;
clcd_write_instruction(instruction);
}

## Slide 9: clcd.c (cont)
void clcd_put_char(char c)
{
clcd_wait();
CLCD_RS=1;CLCD_RW=0;
CLCD_DB=c;CLCD_E=1;CLCD_E=0;
}
void clcd_put_string(char *s)
{
while(*s!=0){clcd_put_char(*s);s++;}
}

## Slide 10: clcd.c (cont)
void clcd_put_byte(unsigned char byte_data)
{
clcd_put_char(ASCII[byte_data/16]);
clcd_put_char(ASCII[byte_data%16]);
}
void clcd_put_word(unsigned int word_data)
{
clcd_put_byte(word_data/256);
clcd_put_byte(word_data%256);
}

## Slide 11: clcd.c (cont)
void i2s(int i,char *s)
{
char sign;unsigned char len;char *p;
sign='+';len=0;p=s;
if(i<0){sign='-';i=-i;}
do{*s=(i%10)+'0';s++;len++;i/=10;}while(i!=0);
if(sign=='-'){*s='-';s++;len++;}
for(i=0;i<len/2;i++){p[len]=p[i];p[i]=p[len-1-i];p[len-1-i]=p[len];}
p[len]=0;
}
void clcd_put_integer(int i)
{
char s[7];
i2s(i,s);clcd_put_string(s);
}

## Slide 12: clcd-ex.c
#include <at89x51.h>
#define CLCD_RS P2_0
#define CLCD_RW P2_1
#define CLCD_E P2_2
#define CLCD_DB P1
#include "clcd.c"
void main(void)
{
int i;
unsigned char j;
char tmp;
char msg[17]="Hello, 8051! ";
clcd_initialize();
clcd_set_cursor(1,0);
clcd_put_string("Chin-Shiuh Shieh");

## Slide 13: clcd-ex.c (cont)
for(j=0;j<16;j++)
{
clcd_set_cursor(0,0);clcd_put_string(msg);
for(i=-32768;i<32767;i++);
for(tmp=msg[0],i=1;i<16;i++)
msg[i-1]=msg[i];
msg[15]=tmp;
}
clcd_cls();clcd_set_cursor(0,0);clcd_put_string(msg);
clcd_set_cursor(1,0);
clcd_put_byte(12);clcd_put_string("h * ");
clcd_put_byte(34);clcd_put_string("h = ");
clcd_put_integer(12*34);
while(1==1);
}