## Slide 1: Keypad Functions for SDCC
Chin-Shiuh Shieh

## Slide 2: Keypad Functions for SDCC
keypad.c is a library of 4x4 keypad functions for Small Device C Compiler (SDCC).
keypaddm.c is an example of controlling DC motor using keypad.
keypadsm.c is an example of controlling stepper motor using keypad.

## Slide 3: Keypad Functions for SDCC (cont)

## Slide 4: keypad.c
// Keypad functions (with 74C922)
// by Chin-Shiuh Shieh on 2011-04-04
// #define KEYPAD_DO P1
// #define KEYPAD_DA P1_4
#define KEYPAD_NULL 0x10
// Function Prototypes
unsigned char keypad_get_key(void);
unsigned char keypad_get_key_echo(void);
unsigned char keypad_check_key(void);
unsigned char keypad_get_byte(void);
unsigned int keypad_get_word(void);
unsigned int keypad_get_integer();

## Slide 5: keypad.c (cont)
unsigned char keypad_get_key(void)
{
unsigned char key;
KEYPAD_DO|=0x1F;while(KEYPAD_DA==0);
key=KEYPAD_DO;key&=0x0F;
while(KEYPAD_DA==1);return key;
}
unsigned char keypad_get_key_echo(void)
{
unsigned char key;
KEYPAD_DO|=0x1F;while(KEYPAD_DA==0);
key=KEYPAD_DO;key&=0x0F;
// uart_put_char(ASCII[key]);
// clcd_put_char(ASCII[key]);
while(KEYPAD_DA==1);return key;
}

## Slide 6: keypad.c (cont)
unsigned char keypad_check_key(void)
{
unsigned char key;
KEYPAD_DO|=0x1F;
if(KEYPAD_DA==1)
{key=KEYPAD_DO;key&=0x0F;while(KEYPAD_DA==1);return key;}
else
return KEYPAD_NULL;
}
unsigned char keypad_get_byte(void)
{
return(keypad_get_key_echo()*16+keypad_get_key_echo());
}
unsigned int keypad_get_word(void)
{
return(keypad_get_byte()*256+keypad_get_byte());
}

## Slide 7: keypad.c (cont)
unsigned int keypad_get_integer(void)
{
unsigned int value=0;
unsigned char key;
while((key=keypad_get_key())<0x0A)
{
// uart_put_char(ASCII[key]);
// clcd_put_char(ASCII[key]);
value=value*10+key;
}
return value;
}

## Slide 8: keypaddm.c

## Slide 9: keypaddm.c (cont)
#include <at89x51.h>
#define KEYPAD_DO P1
#define KEYPAD_DA P1_4
#include "keypad.c"
void main(void)
{
__bit dm_direction=0;
unsigned char dm_speed=0;
unsigned char key;
unsigned char i;
while(1==1)
{
key=keypad_check_key();
if(key<=9)dm_speed=key*10; // ‘0’~’9’ for Speed Control
if(key==10)dm_direction=0; // ‘A’ for Turn to Right
if(key==11)dm_direction=1; // ‘B’ for Turn to Left

## Slide 10: keypaddm.c (cont)
if(dm_speed==0) // Turn Off
{
P2_0=1;P2_1=1;P2_2=0;P2_3=0;
}
if(dm_direction==0) // Turn to Right
{
P2_1=1;P2_2=0;P2_0=0;
P2_3=1;for(i=0;i<dm_speed;i++);
P2_3=0;for(i=dm_speed;i<100;i++);
}
else // Turn to Left
{
P2_0=1;P2_3=0;P2_1=0;
P2_2=1;for(i=0;i<dm_speed;i++);
P2_2=0;for(i=dm_speed;i<100;i++);
}
}
}

## Slide 11: keypadsm.c

## Slide 12: keypadsm.c (cont)
#include <at89x51.h>
#define KEYPAD_DO P1
#define KEYPAD_DA P1_4
#include "keypad.c"
void main(void)
{
unsigned char sm_control=0x01;
unsigned int sm_step=0;
__bit sm_direction=0;
unsigned int i;

## Slide 13: keypadsm.c (cont)
while(1==1)
{
sm_step=keypad_get_key()*100+keypad_get_key()*10+keypad_get_key();
// Step Control: 000~999
if(keypad_get_key()==10)sm_direction=0;else sm_direction=1;
// Key 'A' for Turn to Right, others for Turn to Left
while(sm_step>0)
  {
  if(keypad_check_key()==12)break; // Key 'C' for abort
  if(sm_direction==0){sm_control/=2;if(sm_control==0)sm_control=8;}
  if(sm_direction==1){sm_control*=2;if(sm_control>8)sm_control=1;}
  P0=sm_control;for(i=0;i<5000;i++);
  sm_step--;
  }
}
}