## Slide 1: UART Functions for SDCC
Spring 2011
C.-S. Shieh, EC, KUAS, Taiwan
<number>
Chin-Shiuh Shieh

## Slide 2: UART Functions for SDCC
Spring 2011
C.-S. Shieh, EC, KUAS, Taiwan
<number>
uart.c is a library of Universal Asynchronous Receiver/Transmitter (UART) functions for Small Device C Compiler (SDCC), including character, string, integer I/O.
Tera Term Pro V2.3, by T. Teranishi, is a free software terminal emulator supporting serial port (RS232) and TCP/IP (telnet) connections.

## Slide 3: UART Functions for SDCC (cont)
Spring 2011
C.-S. Shieh, EC, KUAS, Taiwan
<number>

## Slide 4: uart.c
Spring 2011
C.-S. Shieh, EC, KUAS, Taiwan
<number>
// UART functions for SDCC by Chin-Shiuh Shieh on 2011-04-04
// uart_initialize() should be called before using UART
// UART function prototypes
void uart_initialize(void);
void uart_put_char(char c);
char uart_get_char(void);
char uart_get_char_echo(void);
void uart_put_string(char *s);
void uart_get_string(char *s);
void uart_i2s(int i,char *s); // Convert Integer to String
int uart_s2i(char *s); // Convert String to Integer
void uart_put_integer(int i);
int uart_get_integer();
void uart_put_byte(unsigned char byte_data);
void uart_put_word(unsigned int word_data);
__code char uart_ASCII[]="0123456789ABCDEF";

## Slide 5: uart.c (cont)
Spring 2011
C.-S. Shieh, EC, KUAS, Taiwan
<number>
void uart_initialize(void)
{
PCON&=0x7F; // Clear SMOD of PCON, No Double Baud Rate
TMOD&=0x2F;TMOD|=0x20;
// Set Timer1 to 8-bit auto reload mode for Baud Rate Generation
TH1=0xFD; // Set Baud Rate to 9600 bps for 11.0592M Hz
SM0=0;SM1=1; // Set UART to Mode 1 (8-bit UART)
REN=1; // Set REN of SCON to Enable UART Receive
TR1=1; // Set TR1 of TCON to Start Timer1
TI=0;RI=0; // Clear TI/RI to Get Ready to Send/Receive
}

## Slide 6: uart.c (cont)
Spring 2011
C.-S. Shieh, EC, KUAS, Taiwan
<number>
void uart_put_char(char c) // Put Character to UART
{
SBUF=c;
while(TI==0);TI=0;
}
char uart_get_char(void) // Get Character from UART
{
while(RI==0);RI=0;
return SBUF;
}
char uart_get_char_echo(void)
// Get Character from UART with Echo, Require uart_put_char()
{
while(RI==0);RI=0;
uart_put_char(SBUF);
return SBUF;
}

## Slide 7: uart.c (cont)
Spring 2011
C.-S. Shieh, EC, KUAS, Taiwan
<number>
void uart_put_string(char *s)
// Put String to UART, Require uart_put_char()
{
while(*s!=0){uart_put_char(*s);s++;}
}
void uart_get_string(char *s)
// Get String from UART, Require uart_get_char_echo()
{
while(((*s)=uart_get_char_echo())!=13)s++;
*s=0;
}

## Slide 8: uart.c (cont)
Spring 2011
C.-S. Shieh, EC, KUAS, Taiwan
<number>
void uart_i2s(int i,char *s) // Convert Integer to String
{
char sign;unsigned char len;char *p;
sign='+';len=0;p=s;
if(i<0){sign='-';i=-i;}
do{*s=(i%10)+'0';s++;len++;i/=10;}while(i!=0);
if(sign=='-'){*s='-';s++;len++;}
for(i=0;i<len/2;i++)
{p[len]=p[i];p[i]=p[len-1-i];p[len-1-i]=p[len];}
p[len]=0;
}
void uart_put_integer(int i)
{
char s[7];
uart_i2s(i,s);uart_put_string(s);
}

## Slide 9: uart.c (cont)
Spring 2011
C.-S. Shieh, EC, KUAS, Taiwan
<number>
int uart_s2i(char *s) // Convert String to Integer
{
int i=0;char sign='+';
if(*s=='-'){sign='-';s++;}
while(*s!=0){i=i*10+(*s-'0');s++;}
if(sign=='-')i=-i;
return i;
}
int uart_get_integer()
{
char s[7];
uart_get_string(s);
return uart_s2i(s);
}

## Slide 10: uart.c (cont)
Spring 2011
C.-S. Shieh, EC, KUAS, Taiwan
<number>
void uart_put_byte(unsigned char byte_data)
{
uart_put_char(ASCII[byte_data/16]);
uart_put_char(ASCII[byte_data%16]);
}
void uart_put_word(unsigned int word_data)
{
uart_put_byte(word_data/256);
uart_put_byte(word_data%256);
}

## Slide 11: uart-ex.c
Spring 2011
C.-S. Shieh, EC, KUAS, Taiwan
<number>
#include <at89x51.h>
#include "uart.c"
void main( void )
{
int i,j;
char s[7];
uart_initialize();
uart_put_string("Name: ");uart_get_string(s);uart_put_char('\n');
uart_put_string("Hello, ");uart_put_string(s);uart_put_char('\n');
uart_put_string("i: ");i=uart_get_integer();uart_put_char('\n');
uart_put_string("j: ");j=uart_get_integer();uart_put_char('\n');
uart_put_integer(i);uart_put_string(" * ");
uart_put_integer(j);uart_put_string(" = ");
uart_put_integer(i*j);uart_put_char('\n');
while(1==1);
}