## Slide 1: Keypad Functions for SDCC
Spring 2011
C.-S. Shieh, EC, KUAS, Taiwan
<number>
Chin-Shiuh Shieh

## Slide 2: Keypad Functions for SDCC
Spring 2011
C.-S. Shieh, EC, KUAS, Taiwan
<number>
keypad.c is a library of 4x4 keypad functions for Small Device C Compiler (SDCC).
keypaddm.c is an example of controlling DC motor using keypad.
keypadsm.c is an example of controlling stepper motor using keypad.

## Slide 3: Keypad Functions for SDCC (cont)
Spring 2011
C.-S. Shieh, EC, KUAS, Taiwan
<number>

## Slide 4: keypad.c
Spring 2011
C.-S. Shieh, EC, KUAS, Taiwan
<number>
// Keypad functions (with 74C922)
// by Chin-Shiuh Shieh on 2011-04-04
// #define KEYPAD_DO P1
// #define KEYPAD_DA P1_4
#define KEYPAD_NULL 0x10
// Function Prototypes
unsigned char keypad_get_key(void);
unsigned char keypad_get_key_echo(void);
unsigned char keypad_check_key(void);
unsigned char keypad_get_byte(void);
unsigned int keypad_get_word(void);
unsigned int keypad_get_integer();

## Slide 5: keypad.c (cont)
Spring 2011
C.-S. Shieh, EC, KUAS, Taiwan
<number>
unsigned char keypad_get_key(void)
{
unsigned char key;
KEYPAD_DO|=0x1F;while(KEYPAD_DA==0);
key=KEYPAD_DO;key&=0x0F;
while(KEYPAD_DA==1);return key;
}
unsigned char keypad_get_key_echo(void)
{
unsigned char key;
KEYPAD_DO|=0x1F;while(KEYPAD_DA==0);
key=KEYPAD_DO;key&=0x0F;
// uart_put_char(ASCII[key]);
// clcd_put_char(ASCII[key]);
while(KEYPAD_DA==1);return key;
}

## Slide 6: keypad.c (cont)
Spring 2011
C.-S. Shieh, EC, KUAS, Taiwan
<number>
unsigned char keypad_check_key(void)
{
unsigned char key;
KEYPAD_DO|=0x1F;
if(KEYPAD_DA==1)
{key=KEYPAD_DO;key&=0x0F;while(KEYPAD_DA==1);return key;}
else
return KEYPAD_NULL;
}
unsigned char keypad_get_byte(void)
{
return(keypad_get_key_echo()*16+keypad_get_key_echo());
}
unsigned int keypad_get_word(void)
{
return(keypad_get_byte()*256+keypad_get_byte());
}

## Slide 7: keypad.c (cont)
Spring 2011
C.-S. Shieh, EC, KUAS, Taiwan
<number>
unsigned int keypad_get_integer(void)
{
unsigned int value=0;
unsigned char key;
while((key=keypad_get_key())<0x0A)
{
// uart_put_char(ASCII[key]);
// clcd_put_char(ASCII[key]);
value=value*10+key;
}
return value;
}